## Slide 1: DABANGG: A Case for Noise Resilient Flush-Based Cache Attacks
WOOT 2022
Anish Saxena
Biswabandan Panda
Georgia Institute of Technology
Indian Institute of Technology Kanpur
Indian Institute of Technology Bombay

## Slide 2: Cache Timing-based Attacks
Calibrate
Attack
Leak Information
Brittle Behavior
Low Accuracy
Reduced Stealth

## Slide 3: Outline for Today
What are Flush-based Cache Attacks?
How well do they perform in the wild?
Can we make them resilient to system noise?
What is the impact of DABANGG refinements?

## Slide 4: Outline for Today
What are Flush-based Cache Attacks?
How well do they perform in the wild?
Can we make them resilient to system noise?
What is the impact of DABANGG refinements?

## Slide 5: Primer: Flush-based Cache Attacks
Last Level Cache (LLC)
Shared Address A
Victim Process
Spy Process
t = 0
Phase 1: Flush
clflush A
Phase 2: Wait
load A
Phase 3: Reload (Flush + Reload)
load A
LLC reload Hit
⇒ Victim accessed A!
Shared Address A
Shared Address A
or
Phase 3: Flush (Flush + Flush)
clflush A
LLC clflush Hit
⇒ Victim accessed A!

## Slide 6: Primer: Flush-based Cache Attacks
Last Level Cache (LLC)
Shared Address A
Victim Process
Spy Process
clflush A
load A
Phase 3: Reload (Flush + Reload)
load A
LLC reload Hit
⇒ Victim accessed A!
Shared Address A
Shared Address A
or
Phase 3: Flush (Flush + Flush)
clflush A
LLC clflush Hit
⇒ Victim accessed A!
How do we differentiate a cache hit from a miss?
Calibration!

## Slide 7: Primer: Flush-based Cache Attacks
Calibrate
Iterations
Latency
Cache miss
Cache hit
Threshold
Attack
Measure Latency
Cache hit?
⇒ Victim accessed address!
Profit
Leak crypto keys
Covert channels
Log Keystrokes
And much more
How does it play out in practice?

## Slide 8: Outline for Today
What are Flush-based Cache Attacks?
How well do they perform in the wild?
Can we make them resilient to system noise?
What is the impact of DABANGG refinements?

## Slide 9: Coming back to reality
Expectations
Reality
Intel Xeon W-2145 Skylake
8 cores/ 16 threads
Frequency 1.2 – 4.5 GHz
What’s the root cause? How can we fix this?

## Slide 10: Frequency Scaling and Core Placement
Processor frequency is variable
Core 0
Core 1
Core 2
Core 3
1GHz
1GHz
1GHz
1GHz
4GHz
4GHz
4GHz
4GHz
Core 0
Core 1
Core 2
Core 3
OS can change core placement
Lower latency
Higher latency

## Slide 11: Frequency Scaling and Core Placement
Impact of DVFS
Impact of OS Scheduling
reload hit

## Slide 12: Outline for Today
What are Flush-based Cache Attacks?
How well do they perform in the wild?
Can we make them resilient to system noise?
What is the impact of DABANGG refinements?

## Slide 13: Let’s parameterize system noise
Compute
Memory
IO
C-M-I
Example: crypto functions
Effect: frequency ↑
Example: graph traversal
Effect: frequency ↑
Example: DB query
Effect: frequency
~
L-L-L
L-L-H
.
.
.
H-H-H

## Slide 14: Existing Calibration Techniques
Reload hit
Reload miss
10
20
30
40
50
Iterations
Latency
Threshold?

## Slide 15: DABANGG Calibration
Reload hit
Reload miss
10
20
30
40
50
Iterations
Latency
Miss Mode #1
Miss Mode #2
Miss Mode #3
Miss Mode #4
Hit Mode #1
Hit Mode #2
Hit Mode #3
Hit Mode #4
Hit Modes | 10 | 20 | 30 | 40 | 40
Miss Modes | 25 |  | 35 | 45 | 55

## Slide 16: DABANGG Calibration
Reload hit
Reload miss
10
20
30
40
50
Iterations
Latency
Hit Modes | 10 | 20 | 30 | 40 | 40
Miss Modes | 25 |  | 35 | 45 | 55
5
22.5
27.5
32.5
Lower Thresholds
Upper Thresholds
37.5
42.5
Tuple 1
Tuple 2
Tuple 3

## Slide 17: DABANGG Calibration

## Slide 18: DABANGG+FLUSH+RELOAD Attack Loop
Choose correct threshold tuple
  Dynamically assign threshold
  Periodically Verify
Flush
Wait using compute-intensive loop
  Dynamically set wait period
Reload
  Check for false-positives
  Check for frequent burst-mode accesses
Core 0
Core 1
Core 2
Core 3
sched_yield()
. . . Miss, Hit, Hit, Miss, Hit, Hit, Miss . . .
. . . Miss, Miss, Miss, Hit, Miss, Miss . . .

## Slide 19: DABANGG+FLUSH+RELOAD Attack Loop
Choose correct threshold tuple
  Dynamically assign threshold
  Periodically Verify
Flush
Wait using compute-intensive loop
  Dynamically set wait period
Reload
  Check for false-positives
  Check for frequent burst-mode accesses
Core 0
Core 1
Core 2
Core 3
sched_yield()
. . . Miss, Hit, Hit, Miss, Hit, Hit, Miss . . .
. . . Miss, Miss, Miss, Hit, Miss, Miss . . .
Periodic Verification
Fine-Grained Waiting
Custom Access Patterns

## Slide 20: Outline for Today
What are Flush-based Cache Attacks?
How well do they perform in the wild?
Can we make them resilient to system noise?
What is the impact of DABANGG refinements?

## Slide 21: AES T-Table Private Key Extraction

## Slide 22: DABANGG-enabled AES Private Key Extraction

## Slide 23: DABANGG-enabled AES Private Key Extraction
More experiments in the paper!

## Slide 24: Future Directions
Frequency variation analysis is applicable to:
  Eviction-based attacks
  Prefetch-based attacks
  Any instruction timing-based attack
Hardening detectors against system noise
Integrating DABANGG into existing tools and frameworks

## Slide 25: DABANGG: Noise-Resilient Flush-based Attacks
Get the code, use it, improve it!
https://github.com/DABANGG-Attack/Source-Code
Source Code
Responsible Disclosure
Intel coordinated with us in 2020 and allowed us to proceed without an embargo
In the News!
and more
[1] https://thehackernews.com/2020/05/noise-resilient-flush-attack.html
[2] https://isc.sans.edu/podcastdetail.html?id=7018
[3] https://www.securityweek.com/new-technique-improves-effectiveness-timing-channel-attacks
1
2
3
Anish Saxena
anish.Saxena@cc.gatech.edu
Georgia Institute of Technology